Student Name (printed) _______________________  Date ____________

(01-JULY-2020)

Confined Space--Training Quiz

As you watch the video or PowerPoint presentation, complete the statements below.  Your supervisor/ trainer must review the answers with you and answer any questions you may have.

INSTRUCTOR:

1.  You must send a PDF scan of completed quiz with your signature- all pages- to HSE@tdi-bi.com.  A copy of this quiz will be posted on the crewing module (No certificate).

2.  Make a paper copy of sign in sheets and quizzes for the bridge crew to place in binder #11.

3.  If training files are too large to email, make paper copies to take back to the office. Give originals back to the students.

4.  STUDENT- Insist you get your original quiz back.  It serves as proof of your training.

PowerPoint Presentation -- Fill in the blanks:

Part I:  Types of spaces, types of entries, confined spaces registry, hazards, entry team roles & responsibilities

- The 3 types of confined spaces on TDI vessels are:

  - Category 1 = ____________________ Only

  - Category 2 = ____________________  Required

  - Category 3 = Non- Permit ____________________

- The confined space entry team consists of:

  - _______________________ - a responsible person who supervises the team and maintains communications with the bridge

  - _______________________-  must be trained in the use of an SCBA, wear an SCBA and a wire rope lifeline, appropriate clothing and PPE

  - ________________________- must remain outside the confined space to monitor and communicate with the Entrant

  - Stand By _________________- must remain outside the space, wearing full SCBA gear and wire rope lifeline and be ready to assist the Entrant.

- An Emergency Entry means there is no time to ____________________, so there is no atmospheric ______________ and the entrant must use SCBA to breathe.

- In a Permit Entry,  _________________ is used to displace the hazardous atmosphere,

- All the confined/ enclosed spaces on all TDI vessels are listed in the Confined Spaces Register in SOP-GEN-_______.

- A permit is required when any ONE of the following is present:

  - An ___________________ hazard (Real or potential)

  - The potential for entrapment or __________________________

  - A hazardous _____________________________

  - Any other __________________ safety or health hazard

- The main atmospheric hazard on TDI vessels is lack of _____________________.

- Entrapment or engulfment is basically when a substance traps you, crushes you or stops you from _________________.

- A hazardous ___________________ is any tight space in which you could get trapped.

- The Confined Space permit requires the entry team to:

  - _____________________ the potential hazards in a space

  - Conduct a ________________________ on how to accomplish the work, and

  - Have a _____________________    ____________________ ready in case the entrant cannot get himself out of the space.

Part II:

Accessing, testing, ventilation, communication and drills

- When opening a confined space, the opening must be ________________ to prevent accidental falls into the opening.

- Put up barricades or _________________ to protect your coworkers.

- The goal of ventilating a space is to get all the ________   _________   out.

- Ventilate from the ______________ up long enough to displace all the air at least ____________.

- Make sure the air you are putting in is _____________________.

- Gas testers on TDI vessels only test for ____________________.

- Be sure to test the atmosphere at all different __________________ of the space.

- Lower the oxygen tester all the way to the  _____________________ of the space.

- If using radios to communicate, make sure they __________ in the space and the batteries are fully charged.

- The Attendant must be alert for:

  - Changes in  _____________________

  - An unexpected ____________ in work

  - New or changing __________________

- Do not perform work that was not on the ______________________.

- The main difference between drills on the US Flag vessels and our Vanuatu vessels is that all US vessel drills are for _________________________ Entry only.

Print Student Name:  _________________________________

Print name of trainer or supervisor who reviewed answers with student:

____________________________