Trainee Name (printed)  ANSWER KEY          	  Date ____________

(01 July 2020)

Confined Space--Training Quiz

Part I:  Types of spaces, types of entries, confined spaces registry, hazards, entry team roles & responsibilities

- The 3 types of confined spaces on TDI vessels are:

  - Category 1 = __Emergency__ Only

  - Category 2 = __Permit____  Required

  - Category 3 = Non- Permit ___Required_______

- The confined space entry team consists of:

  - __Supervisor____ - a responsible person who supervises the team and maintains communications with the bridge

  - _____Entrant________-  must be trained in the use of an SCBA, wear an SCBA and a wire rope lifeline, appropriate clothing and PPE

  - ___Attendant_____- must remain outside the confined space to monitor and communicate with the Entrant

  - Stand By __Rescuer____- must remain outside the space, wearing full SCBA gear and wire rope lifeline and be ready to assist the Entrant.

- An Emergency Entry means there is no time to _ventilate____, so there is no atmospheric __testing___ and the entrant must use SCBA to breathe.

- In a Permit Entry,  _(forced air) ventilation___ is used to displace the hazardous atmosphere,

- All the confined/ enclosed spaces on all TDI vessels are listed in the Confined Spaces Register in SOP-GEN-_004______.

- A permit is required when any ONE of the following is present:

  - An __atmospheric__ hazard (Real or potential)

  - The potential for entrapment or ____engulfment_____

  - A hazardous ___configuration________

  - Any other ___serious____ safety or health hazard

- The main atmospheric hazard on TDI vessels is lack of ___oxygen_____.

- Entrapment or engulfment is basically when a substance traps you, crushes you or stops you from _breathing_.

- A hazardous __configuration__ is any tight space in which you could get trapped.

- The Confined Space permit requires the entry team to:

  - __Evaluate______ the potential hazards in a space

  - Conduct a ___JSA_____ on how to accomplish the work, and

  - Have a __Rescue______    _______Plan______ ready in case the entrant cannot get himself out of the space.

Part II:

Accessing, testing, ventilation, communication and drills

- When opening a confined space, the opening must be _guarded__ to prevent accidental falls into the opening.

- Put up barricades or _warnings__ to protect your coworkers.

- The goal of ventilating a space is to get all the _bad__   __air____   out.

- Ventilate from the _bottom_ up long enough to displace all the air at least _once___.

- Make sure the air you are putting in is ___clean________.

- Gas testers on TDI vessels only test for ___oxygen______.

- Be sure to test the atmosphere at all different _levels___ of the space.

- Lower the oxygen tester all the way to the  ___ bottom___ of the space.

- If using radios to communicate, make sure they _work_ in the space and the batteries are fully charged.

- The Attendant must be alert for:

  - Changes in  ___behavior____

  - An unexpected __stop__ in work

  - New or changing _hazards_______

- Do not perform work that was not on the ____JSA__________.

- The main difference between drills on the Brooks McCall and our Vanuatu vessels is that all Brooks McCall drills are for ______Emergency___ Entry only.

Print Student Name:  _________________________________

Print name of trainer or supervisor who reviewed answers with student:

____________________________