APOS HiPaP 350 Default Range Adjustment Procedure

- PURPOSE

The purpose of this procedure is to detail the steps involved for all Laptop Computers requiring Adjustment for the HIPAP Transducer Settings.

- SCOPE

This procedure applies to all employees within the Organization.

- RESPONSIBILITY AND AUTHORITY

The Technical Director has the responsibility and authority for ensuring that this procedure is effectively implemented.

- Procedure

Begin with logging in. Scroll over to the User tab and select Logon...

Select service and the password is 1997

Once that is done scroll over to the area where the beacons are being displayed and Right Click,

you should see a drop menu appear.

Scroll down to properties in the drop menu.

If you observe down below where Transducer Transmit Power & Max Range is located you

will notice that both are set to default.

Deselect the default checked box (Transducer Transmit Power) area. Now you would see that

you’re able to select from Maximum to minimum.

Select maximum, once that is done scroll over to the Max Range area and deselect the default

checked box.

Now you’re able to select and enter your desired range. Set the max range from the Default

1500 to 3000.

After changing your max range to 3000, Hit Apply.

Your screen should look exactly like this.

See Following Screen shot illustrations for adjusting advanced settings.

To modify the beacon channels for depth signal loss at 500m (shallow water), increase the interrogation rate

Up to 1.3 – the default is 1.0).

If necessary, Go to the event view are verify if any errors are being displayed. When you do a core can you go to Configure > Interface to Transceiver 1 and tick the Show IO debug. A window with the raw data should come up, go to the very top left corner and click. Then go save to file and remember to un-tick it when finished or it will fill up the hard drive.

- RELATED DOCUMENTATION

- Revisions

| Section | Description | Date | Approved by: |
| --- | --- | --- | --- |
|  | Initial Release | 1-12-12 | G. Patterson |
|  | Add Advanced Screen shots | 1-13-12 | G. Patterson |