HIPAP or HPR400 APOS Computer Calibration Replacement Instructions

- PURPOSE

The purpose of this procedure is to detail the steps involved for all Laptop Computers requiring Calibration Information for Setup on APOS Replacement Computer.

- SCOPE

This procedure applies to all employees within the Organization.

- RESPONSIBILITY AND AUTHORITY

The Technical Director has the responsibility and authority for ensuring that this procedure is effectively implemented.

- Procedure

  - Instructions for HIPAP > Select User > Log on as “Service” > Password “1997”.  See Figure 1.

  - Instructions for HPR 400 > Go to Step 5.0

Figure 1

  - Verify the Geographic Positioning and CNAV antenna offsets.  See Figures1 & 2.

Figure 2

Figure 3  Note: Be sure to keep UTM in Auto mode, unless otherwise required.

  - Verify the Forward, Starboard, Height values are entered and the Roll/Pitch Correction is checked

in figure 3 above.

  - Select Configure > Transceiver > Select “Configure under Transducer” transducer head offsets.  See figures 4-6.

Figure 4

Figure 5

Figure 6

  - In same screen > Enter the Pitch, Roll, Gear Rotation, and Vertical depth from the previous APOS Computer.  These values are the actual calibration values needed. See figure 7.

Figure 7  Note:  These values are examples only, Use the values from the previous Calibrated APOS Computer.

- Instructions for HPR 400:

  - Select User > Log on as “Service” > Password “1997”.  See Figure 8.

Figure 8

  - Verify the Geographic Positioning and CNAV antenna offsets.  See Figures 9 & 10.

Figure 9

Figure 10  Note: Be sure to keep UTM in Auto mode, unless otherwise required.

  - Verify the Forward, Starboard, Height values are entered and the Roll/Pitch Correction is checked

in figure 10 above.

  - Select Configure > Transceiver > Select “Configure under Transducer” transducer head offsets.  See figures 11-13.

Figure 8

Figure 9

Figure 10

  - In the same screen Enter the Pitch, Roll, Gear Rotation, and Vertical depth from the previous APOS Computer.  These values are the actual calibration values needed. See figure 6.

Figure 11

  - Select OK > Enter the Pitch, Roll, Gear Rotation, and Vertical depth from the previous APOS Computer.  These values are the actual calibration values needed. See figure 11.

Figure 12

Figure 13  Note:  These values are examples only, Use the values from the previous Calibrated APOS Computer.

- RELATED DOCUMENTATION

- Revisions

| Section | Description | Date | Approved by: |
| --- | --- | --- | --- |
|  | Initial Release | 1-16-14 | G. Patterson |

# Text boxes

Verify NEMA ExtInterface1 is selected > Verify CNAV offsets are Entered and are correct per the vessel.  Verify the “Pitch & Roll correction” is checked.

Verify NEMA ExtInterface1 is selected > Verify CNAV offsets are Entered and are correct per the vessel.  Verify the “Pitch & Roll correction” is checked.