Brooks McCall Navigation pre-start checklist

Job Number_____________, Job sponsor_____________, Job objective___________________________

Party Chief__________________, Day Navigator___________________, Night Navigator_____________

What systems will you be using on this project?

Winfrog_____   USBL_____     Sub Bottom Profiler________   Single Beam________

There are Two GPS receivers on the Proteus that feed into Winfrog

- Primary GPS: C-Nav 3050 serial number 14123. current baud rate__________, com port_______

Offsets for this GPS: Forward____________, Starboard_____________, Above_______________

Are these entered in the vehicle devices in Winfrog? _____ In the configuration for APOS?_____

(See below for details on where these offsets go)

- Secondary GPS Trimble: current baud rate (as GPS)_________, com port__________

Offsets for this GPS: Forward____________, Starboard_____________, Above_______________

Are these entered in the vehicle devices in Winfrog? _____

There are Two gyros on the Brooks McCall that feed into Winfrog assuming someone has not taken them

- Primary Gyro: Meridian Gryo under the nav desk.  This takes an hour to become accurate after the power has been turned on.

Com Port__________, Baud rate ___________.

- Secondary Gyro: bridge three-antenna satellite gyro  Com Port__________, Baud rate ________.

Wind sensor: Windsonic.

Com port__________, Baud rate _____________

Sounder: Bridge Fruno fish finder.

Com port__________, Baud rate______________

Offsets for this GPS: Forward____________, Starboard_____________, Above_______________

Winfrog setup

Have the following files been received?   Waypoints_____, Nav log_______, loadable maps______,

Was a new project created?  ______     Are the geodetics confirmed with Mike?  ________

New waypoints entered?________   Does the bridge have copies of the waypoints etc…?_________

Have the clients signed off on the Geodetics and waypoints?  ____________

Are the offsets entered in the Vehicle Device window for GPS and Sounder?_____________

Are the correct channels added for devices on the “corer” vehicle?_________

APOS setup

What beacons are on board? ___________, ____________, ____________, ____________, __________

____________, ____________, any special beacons? ___________, ______________, _____________

What channel/s will be used? ____________________________________________________________

Proper offsets entered for GPS antenna: System(Geographic Positioning Setup.  ___________

Proper offsets entered for transducer: Configure( Transceiver( Transducer configure ___________

Will the PEP allow for using the previous Calibration? ___________  If not;  has an appropriate site (500m deep) site been selected for calibration?_________ Does bridge know_______

For APOS calibration see the HiPAP Calibration powerpoint

Sub bottom Profiler

Will chirp be used on this project?  ___________.  How long are the lines?____________________

Is there a requested heading or will best seas be used?____________________________________

Is there a CHIRP tab in the nav log?__________.  Are depths provided?____________________

Is the system set up?____________, monitor_____, mouse______, keyboard___________

Where will the .JSF files be saved____________________.  Jpeg images_______________________

Completed by___________________________     Date:_______________________