VESSEL SHUTDOWN/STARTUP CHECKLIST

#### TDI Brooks Research Vessels

Circle and name as applicable

| Date | Brooks McCall | Gyre | Proteus |
| --- | --- | --- | --- |
| Master OFF |  | Master ON |  |

# BRIDGE LOG ENTRY

Make Last Bridge Log Entry to read –

“Vessel secure alongside at __________, entering a “standby – waiting for work” period with reduced staffing or shore maintenance personnel.

Who….departed vessel on (date/time).

Who….remaining on board.

Main engines (and whatever else) secured.  Vessel transferred to shore power.

Security of vessel rests with ….(?  PFSO, who on board, port engineer, 2nd etc?)

- Master’s Handover, Vessel Condition report completed, filed, and available (here?)

- Chief Engineer’s Handover completed, filed, and available (here?)

- Party Chief Cruise Completion report completed, file, and available (here?)

- Outside entrances and restricted areas locked per Ship Security Plan.

SHIP SECURITY___________

Declaration of Security Executed with______________________________ Date______________

PFSO Name ___________________________________phone # _______________________

Company Security Officer – Roger Fay – Notified_______________y/n

Cell (979) 220-3807, office (979) 693-3446, hm (979) 691-8600

rogerfay@tdi-bi.com, drskyking2@gmail.com, cso@tdi-bi.com

LOGGED ENTRIES COMPLTETED_____________

Oil Record Book – all entries complete, CE signature, Master page sign/close out_________

Garbage Record Book – garbage emptied, signed entry made________

Night Orders, complete to date, signed by all_____________

Notice to Mariners to date, logged_______                corrections made thru _________

NS5 – completed work orders closed, replicated___________

CHECK BEFORE DEPARTING SHIP

____ Deck Equipment stored and secured (retracted rams, covers on boat, winches, ladders.

____ Security locks on all doors, single entry point.  CCTV cameras in position.

____ Deck lights lit.  Interior bridge lights off.

____ Bridge Electronics and computers powered off.

____ Bilge and Freezer alarms tested and on.

____ Stuffing tubes tightened.

____ Bilge level noted, recorded.

____ To shore Power OR ____ Powered down

WHEN PREPARING FOR RESTART

____ Review Last Master’s Handover report

____ Request NTMs from email.

____ Safety Equipment check – the lists. (MOBASS, FFE, GA,

____ Unlock all doors

____ Power Electronics

____ Gyro?

____ Off Shorepower?

Signature Departing Master   ______________________________________       date_________

Signature of  Master Signing On ________________________________________date_________

Original: in Bridge Log

Scan as pdf and email to:

Port Engineer portengineer@tdi-bi.com

Distribution – DPA@tdi-bi.com

Ship’s file – file@tdi-bi.com